## Slide 1: Chapter 15
Scheduling

## Slide 2: Scheduling
Scheduling: Establishing the timing of the use of equipment, facilities and human activities in an organization
Answering “when” question for activities
Build A
A Done
Build B
B Done
Build C
C Done
Build D
Ship
JAN
FEB
MAR
APR
MAY
JUN
On time!

## Slide 3: High-Volume Systems
Flow system: High-volume system with Standardized equipment and activities.
  Assembly line balancing
  Auto, computer industry
Flow-shop scheduling
  Due to Repetition, scheduling is not a big issue
Project scheduling
Work Center #1
Work Center #2
Output

## Slide 4: High-Volume Success Factors
Process and product design
Preventive maintenance
Rapid repair when breakdown occurs
Optimal product mixes
  Most profit subject to capacities = LP
Minimization of quality problems
Reliability and timing of supplies

## Slide 5: Intermediate-Volume Systems
Outputs are between standardized high-volume systems and made-to-order job shops
Economic run size:

## Slide 6: Scheduling Low-Volume Systems
Low volume systems
  Minimal repetition
  Schedule from scratch every time
Loading - assignment of jobs to process centers
Sequencing - determining the order in which jobs will be processed
  Sequencing vs. Scheduling

## Slide 7: Gantt Load Chart
Gantt chart - used as a visual aid for loading and scheduling
  Resources into rows
  Time periods into columns

## Slide 8: Loading
Infinite loading: unlimited capacity, like MRP
Finite loading: consider capacity
Schedule construction
  Vertical loading
    Load on 1 work center with different jobs at once
  Horizontal loading
    Load operations of 1 job to all work center at once
Forward scheduling
  Too much wip
Backward scheduling
  Risky

## Slide 9: Sequencing
Priority rules: Simple heuristics used to select the order in which jobs will be processed.
Job time: Time needed for setup and processing of a job.
It includes set up time unless setup times are sequence dependent
Everything is #1 Priority

## Slide 10: Priority Rules
FCFS - first come, first served
SPT - shortest processing time
EDD - earliest due date
CR - critical ratio
        =time remaining / processing time
S/O - slack per operation
        =slack remaining / # of operations remaining
Rush - emergency

## Slide 11: Performance measures
Flow time of a job: Duration of time from a job enters into the system until it leaves
Lateness of a job: Amount by which completion date exceeds due date. Could be negative.
Tardiness=max(lateness,0)
Makespan: total time needed to finish a group of jobs
Average number of jobs until the last is finished:
=Total flow time / Makespan

## Slide 12: Example: Average number of jobs
Jobs: A and B with processing times 10 each
A finishes at 10
Number of jobs
1
2
B finishes at 20
Time
Makespan=20, Total Flow time=10+20
Average number of jobs=30/20
Average number of jobs

## Slide 13: Example: Sequencing rules
Jobs | Processing time | DD=Due date
A | 11 | 61
B | 29 | 45
C | 31 | 31
D | 1 | 33
E | 2 | 32

## Slide 14: Ex: FCFS
Jobs | Proc.time | Flow time | DD | Late | Tardy
A | 11 | 11 | 61 | -50 | 0
B | 29 | 40 | 45 | -5 | 0
C | 31 | 71 | 31 | 40 | 40
D | 1 | 72 | 33 | 39 | 39
E | 2 | 74 | 32 | 42 | 42
Total |  | 268 | 202 | 66 | 121
Aver. |  | 53.6 | 40.4 | 13.2 | 24.2

## Slide 15: Ex: SPT to minimize the total flow time
Jobs | Proc.time | Flow time | DD | Late | Tardy
D | 1 | 1 | 33 | -32 | 0
E | 2 | 3 | 32 | -29 | 0
A | 11 | 14 | 61 | -47 | 0
B | 29 | 43 | 45 | -2 | 0
C | 31 | 74 | 31 | 43 | 43
Total |  | 135 | 202 | -67 | 43
Aver. |  | 27.0 | 40.4 | -13.4 | 8.6

## Slide 16: Ex: EDD to minimize the maximum lateness
Jobs | Proc.time | Flow time | DD | Late | Tardy
C | 31 | 31 | 31 | 0 | 0
E | 2 | 33 | 32 | 1 | 1
D | 1 | 34 | 33 | 1 | 1
B | 29 | 63 | 45 | 18 | 18
A | 11 | 74 | 61 | 13 | 13
Total |  | 235 | 202 | 33 | 33
Aver. |  | 47.0 | 40.4 | 6.6 | 6.6

## Slide 17: Example summary
235/74=3.17
6.6
47
EDD
135/74=1.82
8.6
27
SPT
268/74=3.62
24.2
53.6
FCFS
Average Number of Jobs at the Work Center
Average Tardiness (days)
Average Flow Time (days)
Rule

## Slide 18: Two Work Center Sequencing
Johnson’s Rule: technique for minimizing completion time for a group of jobs to be processed on two machines or at two work centers.
Minimizes total idle time and the makespan
Several conditions must be satisfied

## Slide 19: Johnson’s Rule Conditions
Job time must be known and constant
Job times must be independent of sequence
Jobs must follow same two-step sequence
Job priorities cannot be used
All units must be completed at the first work center before moving to the second

## Slide 20: Johnson’s rule
1. Select a job with the shortest processing time
  If the processing time is on the first workcenter
  Schedule the job right after the already scheduled at the beginning of the list
  If the processing time is on the second workcenter
  Schedule the job right before the already scheduled at the end of the list
2. Cross out the scheduled job and go to 1

## Slide 21: Example: Johnson’s rule
Job | Processing time on 1 | Processing time on 2
A | 15 | 25
B | 8 | 6
C | 12 | 4
D | 20 | 18

## Slide 22: The sequence that minimizes the makespan A - D - B - C
15
25
20
18
8
6
12
4
15
15
35
40
43
58
55
64
68
15
13
Idle time = 28
Makespan = 68
MC1
MC2

## Slide 23: Sequence dependent set up times
Set up is basically changing the work center configuration from the existing to the new
Set up depends on the existing configuration
Set up time of an operation depends on previous operation done on the same work center
Which sequence minimizes total set up time?
There are too many sequences!

## Slide 24: Scheduling Service Operations
Bottleneck operations
Appointment systems
  Controls customer arrivals for service
    Consider patient scheduling
Reservation systems
  Estimates demand for service
Scheduling the workforce
  Manages capacity for service
Scheduling multiple resources
  Coordinates use of more than one resource